## Slide 1
Peter Jandzio, Mining Engineering Manager March, 2023
Wambo
Respirable Crystalline Silica Dust

## Slide 2: Wambo
Wambo is a combined open-cut and underground mine
Located in the Hunter Valley of New South Wales, Wambo is a well established premium thermal coal mine
Wambo primarily exports to Japan, Korea and China.
In 2022, Wambo complex mined 7.3 million tons of ROM coal.
Wambo employees
  65 Staff
  113 Workforce
  452 UWJV
Wambo UG - Longwall
2
Wambo Opencut

## Slide 3: Wambo Underground
Mining History
Multi Seam UG:
Wollemi (Whybrow)
Homestead (Whybrow)
North Wambo (Wambo)
South Bates (Whybrow)
South Bates (Wambo)
South Bates Extended (Whybrow)
United (Glencore) (Arrowfield)
More challenging mining areas with lower margins (Natural progression) – easy coal taken

## Slide 4: Wambo UG Airborne Dust Results 2022
Respirable Dust
130 results
0 Exceedances
Respirable Crystalline Silica
125 results
28 Exceedances
Inhalable Dust
38 results
0 Exceedance
168
workers sampled
28
Exceedances
Notes: Blair Jackson – or delegate

## Slide 5: The Problem
Exposing our workers to unacceptable levels of dust which may cause lung disease later in life impacting their quality of life or life expectancy
Repeated respirable silica samples above 0.05 mg/m3
Multiple failures on resamples
Multiple persons failed on single crew
  Entire LW crew above limit
Under the microscope from regulators and coal services
  Interventions

## Slide 6: Wambo UG Airborne Dust Results Workers Sampled 2022
Notes: Blair Jackson – or delegate

## Slide 7: Wambo UG Average Respirable Crystalline Silica Longwall
Notes: Blair Jackson – or delegate

## Slide 8: Information
Based on 2022 data, Recently we have a history of cutting a significant amount of stone
Increased exposures to crystalline silica:
Decreasing seam thickness
Cutting of stone and clay bands
Stone on the AFC/BSL/Crusher
Stone intrusions and faulting
Driving stone roadways – belt chambers & overcasts
Loading out while cutting stone
Handling dry cement-based products
Roadway dust
Float dust
Transfer points
Notes: Blair Jackson – or delegate

## Slide 9: Seam thickness / Dates of mining / Structure
2.1-2.3m
2.3-2.6m
2.6-2.9m
2.6 -3.2m
2.3-2.5m
2018
2022

## Slide 10: Mine Working Section - LW
A Ply
B Ply
C Ply
Roof
Clay Band – 0.3m
Claystone / Sandstone –
HARD + ABRASIVE
1m Approx.
0.8m – 1.2m Approx.
Working Section – 2.3m – 2.5m
Floor
35.3 – 39.5% silica
5.5 – 17.3% silica
18.0 – 33.5% silica
4.0 – 12.1% silica
11.5 – 32.7% silica
Claystone

## Slide 11: Geology / Structure
Highly structured mining area
  Highly Variable
  Unpredictable
Roof and floor is sometimes cut to grade horizon through faults
Roof graded into gate roads
LW22 face mapping – Fault in TG roof stone required to be cut

## Slide 12: Example – Stone roof intrusion LW22

## Slide 13: LW Faulting

## Slide 14: LW Faulting

## Slide 15: LW Dust Control Improvements / Actions
Engineering Controls:
Installation of mimic MG DCB – advance 1 + 2 shield from intake side
Homotropal ventilation LW23
Installation of extra BSL / crusher sprays at entry
Installation of pitch steer automation – LW23
Ventilation shaft – under construction
Cone/fog sprays on AFC/BSL interlace
Administration/PPE Controls:
Shiftly dust inspection verification tool
Training more LW operators to allow better rotation
Trialing different operator rotation techniques
Airborne dust TARPs / review of safe standing zones
Cutting horizon plans
Face mapping
Versaflo

## Slide 16: LW22 Cutting horizon

## Slide 17: Airborne Dust Control Inspection Tool

## Slide 18: Airborne dust tools used onsite
Air XD
AM520i

## Slide 19: Things we do
Report each exceedance, Investigate and implement controls
Airborne dust committee onsite
WHS committee has separate section on airborne dust and results
Maintain an airborne dust action log (Longwall, Dev, O/B and whole of mine)
Sample and verify changes and additional controls using dust monitors
Conduct additional static samples i.e. LW boot end to capture outbye dust when sampling
Systematic approach to ensure control effectiveness
Communicate to workforce regularly

## Slide 20: Challenges for a Mine Manager
People
  Getting individuals to care enough about themselves and others about a problem which may occur in the future
  Getting supervisors / engineers engaged and to prioritise hazard
  She’ll be right mate in some instances / Change behaviour
  “They halved the limit!”
  Not a hazard which can easily been seen or immediate impact
  Behavior around ‘passing samples’ when people aren’t watching
Consultation
  So Important, it is a journey
Thorough Investigations
  Delayed – results / roster / Personnel on leave
  Sometimes actions cannot be implemented in time subsequent resample
  Not a definitive cause in some instances / multiple causes cannot be isolated
Continual Education
  Multiple sources for education – Coal Services Technical / Mine Manager / Undermanagers / regulator
Systematic approach
Striving for ALARP

## Slide 21: Summary
Seeing some improvement
  Positive results
  People's behavior and attitudes towards airborne dust
Continual journey
No silver bullet – ALL controls need to be working for the lowest exposure
It takes an active effort to manage
We will continue to strive to lowest exposure possible

## Slide 22: Questions